## Slide 1: REGISTER TRANSFER AND MICROOPERATIONS
• Register Transfer Language
• Register Transfer
• Bus and Memory Transfers
• Arithmetic Microoperations
• Logic Microoperations
• Shift Microoperations
• Arithmetic Logic Shift Unit

## Slide 2: SIMPLE DIGITAL SYSTEMS
Combinational and sequential circuits can be used to create simple digital systems.
These are the low-level building blocks of a digital computer.
Simple digital systems are frequently characterized in terms of
  the registers they contain, and
  the operations that they perform.
Typically,
  What operations are performed on the data in the registers
  What information is passed between registers

## Slide 3: Digital computer
The internal hardware organization of a digital computer is best defined by specifying
The set of registers it contains and their functions
The sequence of microoperations performed on the binary information stored
The control that initiates the sequence of microoperations

## Slide 4: MICROOPERATIONS (1)
Register Transfer Language
The operations on the data in registers are called microoperations.
The functions built into registers are examples of microoperations
  Shift
  Load
  Clear
  Increment
  …

## Slide 5: ORGANIZATION OF A DIGITAL SYSTEM
- Set of registers and their functions
- Microoperations set
Set of allowable microoperations provided
by the organization of the computer
- Control signals that initiate the sequence of
microoperations (to perform the functions)
Definition of the (internal) organization of a computer
Register Transfer Language

## Slide 6: REGISTER TRANSFER LEVEL
Register Transfer Language
Viewing a computer, or any digital system, in this way is called the register transfer level
This is because we’re focusing on
  The system’s registers
  The data transformations in them, and
  The data transfers between them.

## Slide 7: REGISTER TRANSFER LANGUAGE
Register Transfer Language
Rather than specifying a digital system in words, a specific notation is used, register transfer language
For any function of the computer, the register transfer language can be used to describe the (sequence of) microoperations
Register transfer language
  A symbolic language
  A convenient tool for describing the internal organization of digital computers
  Can also be used to facilitate the design process of digital systems.

## Slide 8: DESIGNATION OF REGISTERS
Register Transfer Language
Registers are designated by capital letters, sometimes followed by numbers (e.g., A, R13, IR)
Often the names indicate function:
  MAR - memory address register
  PC - program counter
  IR - instruction register
Registers and their contents can be viewed and represented in various ways
  A register can be viewed as a single entity:
  Registers may also be represented showing the bits of data they contain
MAR

## Slide 9: DESIGNATION OF REGISTERS
Register Transfer Language
R1
Register
Numbering of bits
Showing individual bits
Subfields
PC(H)
PC(L)
15
8
7
0
- a register
- portion of a register
- a bit of a register
Common ways of drawing the block diagram of a register
7 6 5 4 3 2 1 0
R2
15
0
Designation of a register

## Slide 10: REGISTER TRANSFER
Register Transfer
Copying the contents of one register to another is a register transfer
A register transfer is indicated as
  R2  R1
  In this case the contents of register R1 are copied (loaded) into register R2
  A simultaneous transfer of all bits from the source R1 to the destination register R2, during one clock pulse
  Note that this is a non-destructive; i.e. the contents of R1 are not altered by copying (loading) them to R2

## Slide 11: REGISTER TRANSFER
Register Transfer
A register transfer such as
  R3  R5
  Implies that the digital system has
  the data lines from the source register (R5) to the destination register (R3)
  Parallel load in the destination register (R3)
  Control lines to perform the action

## Slide 12: CONTROL FUNCTIONS
Register Transfer
Often actions need to only occur if a certain condition is true
This is similar to an “if” statement in a programming language
In digital systems, this is often done via a control signal, called a control function
  If the signal is 1, the action takes place
This is represented as:
  P: R2  R1
  Which means “if P = 1, then load the contents of register R1 into register R2”, i.e., if (P = 1) then (R2  R1)

## Slide 13: HARDWARE IMPLEMENTATION OF CONTROLLED TRANSFERS
Implementation of controlled transfer
P: R2 R1
Block diagram
Timing diagram
Clock
Register Transfer
Transfer occurs here
R2
R1
Control
Circuit
Load
P
n
Clock
Load
t
t+1
The same clock controls the circuits that generate the control function
and the destination register
Registers are assumed to use positive-edge-triggered flip-flops

## Slide 14: SIMULTANEOUS OPERATIONS
Register Transfer
If two or more operations are to occur simultaneously, they are separated with commas
  P: R3  R5, MAR  IR
Here, if the control function P = 1, load the contents of R5 into R3, and at the same time (clock), load the contents of register IR into register MAR

## Slide 15: BASIC SYMBOLS FOR REGISTER TRANSFERS
Capital letters Denotes a register MAR, R2
& numerals
Parentheses () Denotes a part of a register R2(0-7), R2(L)
Arrow  Denotes transfer of information R2  R1
Colon : Denotes termination of control function P:
Comma , Separates two micro-operations A  B, B  A
Symbols
Description Examples
Register Transfer

## Slide 16: CONNECTING REGISTRS
Register Transfer
In a digital system with many registers, it is impractical to have data and control lines to directly allow each register to be loaded with the contents of every possible other registers
To completely connect n registers  n(n-1) lines
O(n2) cost
  This is not a realistic approach to use in a large digital system
Instead, take a different approach
Have one centralized set of circuits for data transfer – the bus
Have control circuits to select which register is the source, and which is the destination

## Slide 18: BUS AND BUS TRANSFER
Bus is a path(of a group of wires) over which information is transferred, from any of several sources to any of several destinations.
From a register to bus: BUS  R
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Register A
Register B
Register C
Register D
B
C
D
1
1
1
4 x1
MUX
B
C
D
2
2
2
4 x1
MUX
B
C
D
3
3
3
4 x1
MUX
B
C
D
4
4
4
4 x1
MUX
4-line bus
x
y
select
0
0
0
0
Register A
Register B
Register C
Register D
Bus lines
Bus and Memory Transfers

## Slide 19: How to design
In general, a bus system will multiplex k registers of n bits each to produce an n-line common bus
• This requires n multiplexers – one for each bit
• The size of each multiplexer must be k x 1
• The number of select lines required is log k
Foe example, a commnon bus of 8 registers of 16 bits each requires 16 mux, one for each line in the bus. Mux of 8 data input and three selection lines.

## Slide 20: Example
A digital computer has a common bus system for 16 registers of 32 bits each. The bus is constructed with mux
How many select inputs are there in each mux?
What size of mux are needed?
How many mux are there in bus?

## Slide 21: BUS TRANSFER IN RTL
Bus and Memory Transfers
Depending on whether the bus is to be mentioned explicitly or not, register transfer can be indicated as either
or
In the former case the bus is implicit, but in the latter, it is explicitly indicated
R2 R1
BUS R1, R2  BUS

## Slide 22: MEMORY (RAM)
Bus and Memory Transfers
Memory (RAM) can be thought as a sequential circuits containing some number of registers
These registers hold the words of memory
Each of the r registers is indicated by an address
These addresses range from 0 to r-1
Each register (word) can hold n bits of data
Assume the RAM contains r = 2k words. It needs the following
  n data input lines
  n data output lines
  k address lines
  A Read control line
  A Write control line
data input lines
data output lines
n
n
k
address lines
Read
Write
RAM
unit

## Slide 23: MEMORY TRANSFER
Bus and Memory Transfers
Collectively, the memory is viewed at the register level as a device, M.
Since it contains multiple locations, we must specify which address in memory we will be using
This is done by indexing memory references
Memory is usually accessed in computer systems by putting the desired address in a special register, the Memory Address Register (MAR, or AR)
When memory is accessed, the contents of the MAR get sent to the memory unit’s address lines
AR
Memory
unit
Read
Write
Data in
Data out
M

## Slide 24: MEMORY READ
Bus and Memory Transfers
To read a value from a location in memory and load it into a register, the register transfer language notation looks like this:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Read (= 1) gets sent to the memory unit
  The contents of the specified address are put on the memory’s output data lines
  These get sent over the bus to be loaded into register R1
R1  M[MAR]

## Slide 25: MEMORY WRITE
Bus and Memory Transfers
To write a value from a register to a location in memory looks like this in register transfer language:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Write (= 1) gets sent to the memory unit
  The values in register R1 get sent over the bus to the data input lines of the memory
  The values get loaded into the specified address in the memory
M[MAR]  R1

## Slide 26: SUMMARY OF R. TRANSFER MICROOPERATIONS
Bus and Memory Transfers
A  B Transfer content of reg. B into reg. A
AR DR(AD) Transfer content of AD portion of reg. DR into reg. AR
A  constant Transfer a binary constant into reg. A
ABUS  R1, Transfer content of R1 into bus A and, at the same time,
R2 ABUS transfer content of bus A into R2
AR Address register
DR Data register
M[R] Memory word specified by reg. R
M Equivalent to M[AR]
DR  M Memory read operation: transfers content of
memory word specified by AR into DR
M  DR Memory write operation: transfers content of
DR into memory word specified by AR

## Slide 27: MICROOPERATIONS
Computer system microoperations are of four types:
- Register transfer microoperations
- Arithmetic microoperations
- Logic microoperations
- Shift microoperations
Arithmetic Microoperations

## Slide 28: ARITHMETIC MICROOPERATIONS
Summary of Typical Arithmetic Micro-Operations
Arithmetic Microoperations
  R3  R1 + R2 Contents of R1 plus R2 transferred to R3
  R3  R1 - R2 Contents of R1 minus R2 transferred to R3
  R2  R2’ Complement the contents of R2
  R2  R2’+ 1 2's complement the contents of R2 (negate)
  R3  R1 + R2’+ 1 subtraction
  R1  R1 + 1 Increment
  R1  R1 - 1 Decrement
The basic arithmetic microoperations are
  Addition
  Subtraction
  Increment
  Decrement
The additional arithmetic microoperations are
  Add with carry
  Subtract with borrow
  Transfer/Load
  etc. …

## Slide 29: BINARY ADDER / SUBTRACTOR / INCREMENTER
Binary Adder-Subtractor
Binary Incrementer
Binary Adder
Arithmetic Microoperations

## Slide 30: 4 bit binary adder-subtractor

## Slide 32: Arithmetic Circuits Functions

## Slide 33: ARITHMETIC CIRCUIT
S1
S0
0
1
2
3
4x1
MUX
X0
Y0
C0
C1
D0
FA
S1
S0
0
1
2
3
4x1
MUX
X1
Y1
C1
C2
D1
FA
S1
S0
0
1
2
3
4x1
MUX
X2
Y2
C2
C3
D2
FA
S1
S0
0
1
2
3
4x1
MUX
X3
Y3
C3
C4
D3
FA
Cout
A0
B0
A1
B1
A2
B2
A3
B3
0
1
S0
S1
Cin
S1 S0 Cin Y Output Microoperation
0 0 0 B D = A + B Add
0 0 1 B D = A + B + 1 Add with carry
0 1 0 B’ D = A + B’ Subtract with borrow
0 1 1 B’ D = A + B’+ 1 Subtract
1 0 0 0 D = A Transfer A
1 0 1 0 D = A + 1 Increment A
1 1 0 1 D = A - 1 Decrement A
1 1 1 1 D = A Transfer A
Arithmetic Microoperations

## Slide 34: LOGIC MICROOPERATIONS
Logic Microoperations
Specify binary operations on the strings of bits in registers
  Logic microoperations are bit-wise operations, i.e., they work on the individual bits of data
  useful for bit manipulations on binary data
  useful for making logical decisions based on the bit value
There are, in principle, 16 different logic functions that can be defined over two binary input variables
However, most systems only implement four of these
  AND (), OR (), XOR (), Complement/NOT
The others can be created from combination of these
0 0 0 0 0 … 1 1 1
0 1 0 0 0 … 1 1 1
1 0 0 0 1 … 0 1 1
1 1 0 1 0 … 1 0 1
A B F0 F1 F2 … F13 F14 F15

## Slide 35: LIST OF LOGIC MICROOPERATIONS
List of Logic Microoperations
- 16 different logic operations with 2 binary vars.
- n binary vars → functions
2
2
n
Truth tables for 16 functions of 2 variables and the
corresponding 16 logic micro-operations
Boolean
Function
Micro-
Operations
Name
x 0 0 1 1
y 0 1 0 1
Logic Microoperations
  0 0 0 0 F0 = 0 F  0 Clear
  0 0 0 1 F1 = xy F  A  B AND
  0 0 1 0 F2 = xy' F  A  B’
  0 0 1 1 F3 = x F  A Transfer A
  0 1 0 0 F4 = x'y F  A’ B
  0 1 0 1 F5 = y F  B Transfer B
  0 1 1 0 F6 = x  y F  A  B Exclusive-OR
  0 1 1 1 F7 = x + y F  A  B OR
  1 0 0 0 F8 = (x + y)' F  A  B)’ NOR
  1 0 0 1 F9 = (x  y)' F  (A  B)’ Exclusive-NOR
  1 0 1 0 F10 = y' F  B’ Complement B
  1 0 1 1 F11 = x + y' F  A  B
  1 1 0 0 F12 = x' F  A’ Complement A
  1 1 0 1 F13 = x' + y F  A’ B
  1 1 1 0 F14 = (xy)' F  (A  B)’ NAND
  1 1 1 1 F15 = 1 F  all 1's Set to all 1's

## Slide 36: HARDWARE IMPLEMENTATION OF LOGIC MICROOPERATIONS
0 0 F = A  B AND
0 1 F = AB OR
1 0 F = A  B XOR
1 1 F = A’ Complement
S1 S0
Output
-operation
Function table
Logic Microoperations
B
A
S
S
F
1
0
i
i
i
0
1
2
3
4 X 1
MUX
Select

## Slide 37: APPLICATIONS OF LOGIC MICROOPERATIONS
Logic Microoperations
Logic microoperations can be used to manipulate individual bits or a portions of a word in a register
Consider the data in a register A. In another register, B, is bit data that will be used to modify the contents of A
  Selective-set A  A + B
  Selective-complement A  A  B
  Selective-clear A  A • B’
  Mask (Delete) A  A • B
  Clear A  A  B
  Insert A  (A • B) + C
  Compare A  A  B
  . . .

## Slide 38: SELECTIVE SET
Logic Microoperations
In a selective set operation, the bit pattern in B is used to set certain bits in A
1 1 0 0 At
1 0 1 0 B
1 1 1 0 At+1 (A  A + B)
If a bit in B is set to 1, that same position in A gets set to 1, otherwise that bit in A keeps its previous value

## Slide 39: SELECTIVE COMPLEMENT
Logic Microoperations
In a selective complement operation, the bit pattern in B is used to complement certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)
If a bit in B is set to 1, that same position in A gets complemented from its original value, otherwise it is unchanged

## Slide 40: SELECTIVE CLEAR
Logic Microoperations
In a selective clear operation, the bit pattern in B is used to clear certain bits in A
1 1 0 0 At
1 0 1 0 B
0 1 0 0 At+1 (A  A  B’)
If a bit in B is set to 1, that same position in A gets set to 0, otherwise it is unchanged

## Slide 41: MASK OPERATION
Logic Microoperations
In a mask operation, the bit pattern in B is used to clear certain bits in A
1 1 0 0 At
1 0 1 0 B
1 0 0 0 At+1 (A  A  B)
If a bit in B is set to 0, that same position in A gets set to 0, otherwise it is unchanged

## Slide 42: CLEAR OPERATION
Logic Microoperations
In a clear operation, if the bits in the same position in A and B are the same, they are cleared in A, otherwise they are set in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0 At+1 (A  A  B)

## Slide 43: INSERT OPERATION
Logic Microoperations
An insert operation is used to introduce a specific bit pattern into A register, leaving the other bit positions unchanged
This is done as
  A mask operation to clear the desired bit positions, followed by
  An OR operation to introduce the new bits into the desired positions
  Example
    Suppose you wanted to introduce 1010 into the low order four bits of A: 1101 1000 1011 0001 A (Original) 1101 1000 1011 1010 A (Desired)
    1101 1000 1011 0001 A (Original)
    1111 1111 1111 0000 Mask
    1101 1000 1011 0000 A (Intermediate)
    0000 0000 0000 1010 Added bits
    1101 1000 1011 1010 A (Desired)

## Slide 44: LOGICAL SHIFT
Shift Microoperations
In a logical shift the serial input to the shift is a 0.
A right logical shift operation:
A left logical shift operation:
In a Register Transfer Language, the following notation is used
  shl for a logical shift left
  shr for a logical shift right
  Examples:
    R2  shr R2
    R3  shl R3
0
0

## Slide 45: CIRCULAR SHIFT
Shift Microoperations
In a circular shift the serial input is the bit that is shifted out of the other end of the register.
A right circular shift operation:
A left circular shift operation:
In a RTL, the following notation is used
  cil for a circular shift left
  cir for a circular shift right
  Examples:
    R2  cir R2
    R3  cil R3

## Slide 46: Logical versus Arithmetic Shift
A logical shift fills the newly created bit position with zero:
An arithmetic shift fills the newly created bit position with a copy of the number’s sign bit:

## Slide 47: ARITHMETIC SHIFT
Shift Microoperations
An left arithmetic shift operation must be checked for the overflow
0
V
Before the shift, if the leftmost two
bits differ, the shift will result in an
overflow
In a RTL, the following notation is used
  ashl for an arithmetic shift left
  ashr for an arithmetic shift right
  Examples:
    R2  ashr R2
    R3  ashl R3
sign
bit

## Slide 48: HARDWARE IMPLEMENTATION OF SHIFT MICROOPERATIONS
Shift Microoperations
S
0
1
H0
MUX
S
0
1
H1
MUX
S
0
1
H2
MUX
S
0
1
H3
MUX
Select
0 for shift right (down)
1 for shift left (up)
Serial
input (IR)
A0
A1
A2
A3
Serial
input (IL)